## Slide 1
(a) Show-o2 + KV
fixed graph with standard KV reuse
(b) Exact-DLS KV
selected DLS policy, compatible prefix rebuilds
(c) Stable-Graph KV
DLS off, fixed FFN / token pruning retained
KV reuse follows the execution graph
DepGraph-U (b, c): KV under a selected pruning policy
prefix
Prefill
L1
L2
L3
L4
KV
fixed graph
F
0
R
1
R
2
R
…
one prefill, then new-token forwards
Standard KV under a fixed graph
Select
Rebuild
Reuse
L1
L2
L3
L4
G₀
L1
L2
skip
L4
G₁
KV[G1 ]
append token
F
0
F
1
R
2 … T−1
F
T
Early EOS can leave no reuse
Preserves the selected DLS policy
L1
L2
L3
L4
G*
DLS off
KV[G*]
R
FFN pruning
token pruning
selected fixed pruning remains
F
0
R
1
R
2
R
…
fixed graph, incremental continuation
Policy changed
Outputs may differ
F
full-prefix forward
R
new-token KV forward
skip
DLS layer skip
(b, c): last-position vocabulary projection
(b, c) are alternative KV policies under pruning. F/R stop at EOS. T = DLS interval.
Notes: KV execution policies on Show-o2. Panel (a) is Show-o2 with standard KV enabled under a fixed graph. It illustrates the compatibility case, not a claim that the default released mmu_generate loop already uses incremental KV.
Official baseline context: https://github.com/showlab/Show-o/blob/main/show-o2/models/modeling_showo2_qwen2_5.py , checked 2026-09-22. The released mmu_generate loop (lines 489-523) repeatedly supplies the growing input_embeds without forwarding past_key_values. Standard KV is an existing optimization, not a new contribution of DepGraph-U.
Panels (b) and (c) are DepGraph-U KV management alternatives under a selected pruning policy. The evaluated DLS and fixed FFN/token pruning policies come from FlashU and must be cited in the accompanying paper. They are not native properties of panel (a) or claimed novel pruning algorithms.
Panel (b), Exact-DLS KV, retains the selected DLS policy: phase 0 evaluates the full prefix to select a skip set, phase 1 rebuilds the prefix under that graph, and later phases use new-token forwards with compatible KV. At the next DLS cycle the selection/rebuild schedule repeats. Even repeated selections conservatively rebuild. EOS can end the sequence before reuse. Exactness refers to preservation of the selected DLS execution policy and separately verified paired outputs, not identity with unpruned native Show-o2.
Panel (c), Stable-Graph KV, disables that policy's DLS while retaining its fixed FFN and visual-token pruning. It changes the selected dynamic policy and can change outputs. The fixed graph then allows standard incremental KV after one prefill. This is not itself a new standard-KV algorithm.
Both (b) and (c) use last-position vocabulary projection; its cost contribution is separated in the paper's controls. The diagram alone does not establish a speedup over panel (a).
KV validity also requires compatible active layers, retained token mapping, positions, attention masks, and fixed weights/configuration. The runtime maintains per-layer KV and the stored visual gather map rather than comparing graph signatures.
Sources: paper_rewrite_20260908/appendix_sync_v6_20260922/source/sec/3_method.tex:64-102; remote_experiments/understanding_audit_20260904/method_code/modeling_showo2_qwen2_5.py; remote_experiments/understanding_stable_cap128_20260920/PROTOCOL.json.